## Slide 1: b1000 ALU
ENGR xD52
Eric VanWyk
Fall 2012

## Slide 2: Today
Review Timing with Adders
Construct Adder/Subtractor
Construct ALU

## Slide 3: Full Adder
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
CI
0
1
0
1
0
1
0
1
CO
0
0
0
1
0
1
1
1
S
0
1
1
0
1
0
0
1
 | A | B | Cin
Sum |  |  | 
Cout |  |  | 
Calculate Propogation Delays
Multiple Paths? Choose Worst
Discrete Math!!

## Slide 4: Full Adder
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
CI
0
1
0
1
0
1
0
1
CO
0
0
0
1
0
1
1
1
S
0
1
1
0
1
0
0
1
 | A | B | Cin
Sum | 6 | 6 | 3
Cout | 5 | 5 | 2
Calculate Propogation Delays
Multiple Paths? Choose Worst
Discrete Math!!

## Slide 5: Multi-Bit Addition
 | A | B | Cin
Sum | 6 | 6 | 3
Cout | 5 | 5 | 2
 | AB0 | AB1 | AB2
S0 |  |  | 
C1 |  |  | 
S1 |  |  | 
C2 |  |  | 
S2 |  |  | 
C3 |  |  | 
Using previous slides’ design, find worst prop delay

## Slide 6: Multi-Bit Addition
 | A | B | Cin
Sum | 6 | 6 | 3
Cout | 5 | 5 | 2
 | AB0 | AB1 | AB2
S0 | 6 | - | -
C1 | 5 | - | -
S1 | 5+3 | 6 | -
C2 | 5+2 | 5 | -
S2 | 5+2+3 | 5+3 | 6
C3 | 5+2+2 | 5+2 | 5
Using previous slides’ design, find worst prop delay

## Slide 7: Full Adder as a LUT in Gates
 | A | B | Cin
Sum |  |  | 
Cout |  |  | 
A B Cin
0
0
0
1
0
1
1
1
Only half, slide too small to show Sum
Area Cost?
Speed?

## Slide 8: Full Adder as a LUT in Gates
 | A | B | Cin
Sum | 3 | 3 | 3
Cout | 3 | 3 | 3
A B Cin
0
0
0
1
0
1
1
1
Only half, slide too small to show Sum
Area Cost?
Speed?

## Slide 9: Timing with Alternate Topology
 | A | B | Cin
Sum | 3 | 3 | 3
Cout | 3 | 3 | 3
 | AB0 | AB1 | AB2
S0 |  |  | 
C1 |  |  | 
S1 |  |  | 
C2 |  |  | 
S2 |  |  | 
C3 |  |  | 
Using new prop delays, find total delay

## Slide 10: Timing with Alternate Topology
 | A | B | Cin
Sum | 3 | 3 | 3
Cout | 3 | 3 | 3
 | AB0 | AB1 | AB2
S0 | 3 | - | -
C1 | 3 | - | -
S1 | 3+3 | 3 | -
C2 | 3+3 | 3 | -
S2 | 3+3+3 | 3+3 | 3
C3 | 3+3+3 | 3+3 | 3
Using new prop delays, find total delay

## Slide 11: As a GIANT LUT?
How do we construct 3-bit addition as one unified LUT?
  Width?
  Depth?

## Slide 12: As a GIANT LUT?
How do we construct 3-bit addition as one unified LUT?
  Width? 4 (3 Sum Bits, 1 final carry out bit)
  Depth? 2^(3+3) = 64
Index into table = {b2,b1,b0,a2,a1,a0}
  Rows in table = {b2,b1,b0}+{a2,a1,a0}
  Example: M=010001 stores 010 + 001 = 0011

## Slide 13: As a GIANT LUT!
How expensive is a Depth by Width LUT?
  2^M = Depth
Decoder (M->D)
  M inverters
  D M-input AND gates
  2 Units of Delay
  M+MD space
Decoder -> Bussed Mux
  D*W 2 input AND gates
  W D-input OR gates
  2 Units of Delay
  3DW Space
Bussed Mux -> LUT
  Tie inputs to Constants
  Free!
Total:
  4 Units Delay
  M+MD+3DW Space
  2N+(5N+3)(2^2N) Space

## Slide 14: Adder/Subtractor
A - B = A + (-B) = A + B + 1
A
B
CO
S
+
CI
A
B
CO
S
+
CI
A
B
CO
S
+
CI
A
B
CO
S
+
CI
A
3
B
3
A
2
B
2
A
1
B
1
A
0
B
0
S
3
S
2
S
1
S
0
Subtract
Add Control Line for Subtraction

## Slide 15: ALU: Arithmetic Logic Unit
Computes arithmetic & logic functions based on controls
  Add, subtract
  AND, NAND, OR, NOR, XOR, ==, <, overflow, …
A
B
R
Function
Select
Controls
Zero
Negative
Overflow

## Slide 16: Bit Slice ALU Design
00: OR
10: Add
01: AND
11: Subtract
4:1 Mux
00 01 10 11
S1
S0
Ai
Bi
ALU Output Bus

## Slide 17: Bit Slice ALU Design (cont.)
Route Carries
Overflow, zero, negative
1-bit
Slice
1-bit
Slice
1-bit
Slice
1-bit
Slice
ALU3
ALU2
ALU1
ALU0
ALU[3:0]

## Slide 18: SLT
Set less than: if (A<B) then R = 1, else R = 0
  How do we know if (A<B)
  Interaction w/overflow?
At your Desk:
  Try 2 random examples
  Try 2 corner cases
  Do they all work?
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
+0
+1
+2
+3
+4
+5
+6
+7
-8
-7
-6
-5
-4
-3
-2
-1

## Slide 19: Shifter
Support shift operations: (A << 01101)
Optional shift by one: (A << b0)
Optional shift by two: (A << b1)

## Slide 20: More Shiftings
Chain optional power-of-two shifts
  Sometimes called a logarithmic shifter (gross)
Requires logR(N) layers
  N=32, R=2

## Slide 21: Boardel Shifter
Type(s) of Shift:
  Logical? Arithmetic? Rotate?
Size of Shift:
  1 only? All N?
Placement of Shift:
  As a separate instruction? As an instruction “add-on”?
Size vs Speed?
  Radix?
Start with a “Shift arithmetic left 1 as separate instruction”

## Slide 22: ALU Construction Summary
Brute force approach is full parallel with muxes as wide as the number of operations
Re-use resources for space efficiency
  Slower, Smaller, Narrower
Make a SMALL ALU bit slice that does:
  AND, OR, NAND, NOR, XOR, Add, Subtract