## Slide 1: b10011 Numerical Accuracy
ENGR xD52
Eric VanWyk
Fall 2012

## Slide 2: Acknowledgements
The Great Wikipedia, Finder of Figures

## Slide 3: Today
Manipulating Formulae for Fun and Profit
Polynomial Fits
Newton Raphson

## Slide 4: Manipulating Formulae
Welcome to Algebra 404
  Where Math don’t think it be like it is, but it do.
Use algebra to reformat for “good” execution
  Execution Speed
  Code Size
  Accuracy

## Slide 5: Easy Speed Tweaking
Look for degenerate expensive cases
Look for duplicated effort and eliminate it
Plan your loads / stores carefully!

## Slide 6: Multiplication Tricks
Sometimes, shift-add is cheap
  9x = 8x + x = X<<3 + X
  In Arm and Thumb(2), this is one instruction
  add $r1, $r0, $r0 lsl 3
Two ops, One Instruction?
  Why?
Multiplicands with a small number of active bits

## Slide 7: Booth Encoding
Represent the multiplicand as runs of ones
  X*60d = X * b00111100
Runs of Ones are the difference of powers of 2
  60 = 2^6 – 2^4
  X*60 = X<<6 – X<<4
There are many other fixed multiplicand tricks

## Slide 8: Polynomials
“Human” Form:
Ax^3+Bx^2+Cx^1+Dx^0
How many Multiplies does this use? Adds?
Notes: Multiply : 3+2+1 = 6
Add: 3

## Slide 9: Polynomials
“Human” Form:
Ax^3+Bx^2+Cx^1+Dx^0
How many Multiplies does this use? Adds?
(Paraphrased) Horner’s Scheme
((((Ax)+B)x+C)x+D)
Now how many?
  Registers?
Notes: Multiply : 3+2+1 = 6
Add: 3
Multiply: 3
Add : 3

## Slide 10: Polynomial Approximations
Goal: Approximate a transcendental as a poly
Attempt 1: Taylor Series
Create a LUT for several values of a
  Store f^n(a)/n!
Notes: Powerpoint sucks for formulas

## Slide 11: Polynomial Approximation
How deep should the LUT be?
  Deeper means we are on average closer
  Better approximation for a given number of terms
  But Deeper also means more expensive
  No easy answer 
How do you pick a?
  Right in the middle of your range

## Slide 12: Implementation: Poly/LUT
Find the nearest a in our LUT
  Truncate x, use as index in to table
Load Coefficients
  Sine and Cosine are special: Why?
Calculate with Horner’s Scheme

## Slide 13: Picking Coefficients
Taylor Series optimizes accuracy for x ≈ a
  Largest errors right between LUT points
Statistics has nice ways to optimize RMS error
  Does a better job of spreading the error
  But still not perfect
We care about the worst case error
  I haven’t found a great way to do this yet
  So I just brute force it with an annealing algorithm

## Slide 14: My Method
Prototype with double precision floats
  MATLAB, Python or Wolfram Alpha
  Count adds, mults, loads, etc
Move to integer math
  Python (X,Y)
  Any catastrophic loss of precision? Rearrange
  Anneal coefficients over a weekend
Automagically try several Depth/Power combos

## Slide 15: Approximation “Folding”
Make use of symmetry in your functions
  “Fold” the function in half cuts LUT depth in half!
  Easy for trig functions
One of my favorite assembly language games
  Great practice in number systems and asm tricks

## Slide 16: Approximation Folding
How do you fold 1/x?
  1/x^2? e^x?
These have symmetry…
  But not in the linear way trig does
  Higher order symmetry
1/(x) = 2^-n/(x*2^n)

## Slide 17: Approximation Folding
These symmetries are harder to exploit
Count Leading Zeros
  Quick stand-in for log(2)
  Break spaces into powers of 2
  Shift by the number of leading zeros
  Compensate Later
This helps with limiting calculation Range!
  Optimize for accuracy instead of range

## Slide 18: Group Work
Poly/LUT fit a transcendental function
  (Co)sine, e^x, or something else
  Pick a range
  Pick an accuracy – 24 bits?
Start with a Taylor approximation
  LUT Depth? Number of terms?
  What is your worst case error?
Try annealing a bit
  How much did it improve?
Create and Save Figures!
  We will discuss as a class

## Slide 19: Newton Raphson
Successive approximation to find root of a well behaved function

## Slide 20: Newton Raphson Division

## Slide 21: Newton Raphson Division
Quadratic Convergence
  Each step is twice as accurate as previous!
Hot Diggity!... but
  LUT, with symmetry
Must be within a Basin of Attraction
  Bad initial conditions will never converge

## Slide 22: Newton Raphson 1/sqrt
float Q_rsqrt( float number ) {
long i;
float x2, y;
const float threehalfs = 1.5F;
x2 = number * 0.5F;
y = number;
i = * ( long * ) &y; // evil floating point bit level hacking
i = 0x5f3759df - ( i >> 1 ); // what the fuck?
y = * ( float * ) &i;
y = y * ( threehalfs - ( x2 * y * y ) ); // 1st iteration
// y = y * ( threehalfs - ( x2 * y * y ) ); // 2nd iteration, this can be removed
return y;
}

## Slide 23: Translating to Fixed Point
Floating Point Newton Raphson is easy
  It handles range changes for you
Fixed Point is degenerately bad
  Intermediate steps are all over the place
Use symmetry to tighten up ranges
Be Careful!

## Slide 24: With Remaining Time
Estimate how fast NR division runs in MIPS
  Each iteration cost: ?
Implement for x
  In floating point
Find appropriate IQ for intermediate calculations