## Slide 1: b10010 Behavioral Verilog
ENGR xD52
Eric VanWyk
Fall 2012

## Slide 2: Acknowledgements
BYU ECEn 224: http://ece224web.groups.et.byu.net/lectures/A3%20VERILOG.pdf
Y. N. Patt, UT Austin EE382N Verilog Manual: http://users.ece.utexas.edu/~patt/04s.382N/tutorial/verilog_manual.html
Asic World: Verilog Behavioral Modeling: http://www.asic-world.com/verilog/vbehave1.html
Nestoras Tzartzanis, USC EE577b – Verilog for Behavioral Modeling: http://www-scf.usc.edu/~ee577/tutorial/verilog/verilog_lec.pdf

## Slide 3: Today
Lab 3 is assigned
Intro to Behavioral Verilog
Time in-class for Lab 3

## Slide 4: Review Lab 3 Prep
Quick Discussion: How did it go?
Common Themes?

## Slide 5: Review Lab 3 Prep
Quick Discussion: How did it go?
Common Themes?
Ready to do it in only 12 hours?

## Slide 6: Lab 3 Notes
All about time/expectation management
Good planning is critical

## Slide 7: Review: Structural Verilog
Explicitly define the structure of logic circuits
Engineer responsible for soup-to-nuts
Relatively slow to create
Can produce very small / fast implementations

## Slide 8: What is “Behavioral” Verilog
Higher Level than structural verilog
Define the behavior!
  synthesizer determines structure
Relatively fast to create
Size/speed is up to the synthesizer

## Slide 9: Simple Gates
Structural:
and myAnd(output, input, input)
Behavioral
output <= input & input

## Slide 10: The Register File
This is (almost) Lab 1
  One read port instead of two
  Register 0 is a register
  16 words
It is so tiny and cute!
Where is the mux?
  How to make mux 2?
Where is the decoder?
How do the enables work?
module regFile (clk, regWE, Addr,
DataIn, DataOut);
input clk, regWE;
input[4:0] Addr;
input[31:0] DataIn;
output[31:0] DataOut;
reg [31:0] registers [15:0];
// Synchronous write logic
always @(posedge clk)
if (regWE)
registers[Addr] <= DataIn;
// Asynchronous read logic
assign DataOut = registers[Addr];
endmodule

## Slide 11: Asynchronous Logic
Stuff that happens all the time
assign DataOut = registers[Addr];
“Continuous Assignment”
  Left hand MUST be a wire
What are the dependencies?
When is DataOut re-calculated?
  In Simulation? In “Real Life”?

## Slide 12: Synchronous Logic
always @(posedge clk)
if (regWE)
registers[Addr] <= DataIn;
Stuff that happens when triggered
  Trigger list in the @(______) section
When is this re-calculated?
Notes: Every positive edge of the clock

## Slide 13: Example: A counter
Is this synchronous or asynch?
What does WID do?
How would this look in structure?
module upCnt(cnt, clk, clr);
parameter WID=4;
input clk, clr;
output reg[WID-1:0] cnt;
always @(posedge clk)
if (clr)
cnt <= 0;
else
cnt <= cnt + 1;
endmodule

## Slide 14: Example: A counter rewritten
<= Allows Multiple Assignments
The last one “wins”
module upCnt(cnt, clk, clr);
parameter WID=4;
input clk, clr;
output reg[WID-1:0] cnt;
always @(posedge clk)
begin
cnt <= 0;
if(!clr)
cnt <= cnt + 1;
end
endmodule

## Slide 15: Example: A Weird Counter
How would this look in structure?
One Adder or Two?
How to guarantee one adder?
module Cnt2(cnt,clk,add,op);
parameter WID=4;
input clk, add;
input [WID-1:0] op;
output reg[WID-1:0] cnt;
always @(posedge clk)
if (add)
cnt <= cnt + op;
else
cnt <= cnt + 1;
endmodule

## Slide 16: Example: A Full Adder
{} is Concatenation
Note that a,b,cin are not the same length
“|sum” is a Reduction
More info at http://www-scf.usc.edu/~ee577/tutorial/verilog/verilog_lec.pdf
wire[15:0] sum,a,b;
wire cin, cout, zero;
assign {cout, sum} = a + b + cin;
assign zero = !(|sum);

## Slide 17: Example: Lab 2
Partial example of Lab 2
  Rewritten as an example
Case is an easy way to mux between functions
always @ (posedge clk) begin
case (ctrl)
3'b000: out <= busA + busB;
3'b001: out <= busA - busB;
3'b010: out <= busA ^ busB;
3'b011: out <= busA < busB;
3'b100: out <= busA * busB;
3'b101: out <= busA << busB;
3'b110: out <= busA >> busB;
3'b111: out <= busA >>> busB;
endcase
end
// Props to Jimmy & Ian

## Slide 18: Example: Lab 2
Partial example of Lab 2
  Rewritten as an example
Case is an easy way to mux between functions
What happens when an unwritten case is commanded?
always @ (posedge clk) begin
case (ctrl)
3'b000: out <= busA + busB;
3'b001: out <= busA - busB;
3'b010: out <= busA ^ busB;
3'b011: out <= busA < busB;
3'b100: out <= busA * busB;
3'b101: out <= busA << busB;
3'b110: out <= busA >> busB;
3'b111: out <= busA >>> busB;
endcase
end
// Props to Jimmy & Ian
Notes: The previous value is held

## Slide 19: Example: I don’t care anymore
You can use ? as “don’t care” indicator
Fires for 110 and 111
always @ (posedge clk) begin
case (ctrl)
3'b000: out <= busA + busB;
3'b001: out <= busA - busB;
3'b010: out <= busA ^ busB;
3'b011: out <= busA < busB;
3'b100: out <= busA * busB;
3'b101: out <= 0;
3'b11?: out <= foo;
endcase
end
Notes: The previous value is held

## Slide 20: Example: Seriously, I just don’t
Default fires for all cases not already claimed by other cases
always @ (posedge clk) begin
case (ctrl)
3'b000: out <= busA + busB;
3'b001: out <= busA - busB;
3'b010: out <= busA ^ busB;
3'b011: out <= busA < busB;
3'b100: out <= busA*busB;
default: out = foobar;
endcase
end
Notes: The previous value is held

## Slide 21: Finite State Machines
Track state in a register
reg [3:0] state;
Use the parameter keyword to label cases
  Values need to be unique
  But their specific values don’t matter. (Enum)
parameter IFetch = 4’h0;
parameter Decode = 4’h1;
parameter Store1 = 4’h2;
parameter Store2 = 4’h3;
parameter Load1 = 4’h4;
…

## Slide 22: Finite State Machines
Use a Case Structure for the rest
always @(posedge clk)
case(state)
…
Decode: if( op == 43) state = Store1;
else if( op == 35) state = Load1;
// Control Signals
Store1: state = Store2;
// Control Signals
Store2: state = IFetch;
// Control Signals
…
endcase
IFetch
Decode
Store 1
Load 1
Load 2
Load 3
Store 2
Op = = 43
Op = = 35

## Slide 23: Finite State Machines
With this approach you can directly translate the RTL from the multi-cycle lecture in to a functioning CPU
This creates horribly bloated bitstreams
  Up to humans to help the synthesizer optimize
Add
IF: IReg = Memory[PC]
PC=PC+4
ID: A = RegFile[rs]
B = RegFile[rt]
EX: Result = A + B
MEM:
WB: RegFile[rd] = Result

## Slide 24: Loading Memories from Files
module memory(clk, regWE, Addr,
DataIn, DataOut);
input clk, regWE;
input[9:0] Addr;
input[31:0] DataIn;
output[31:0] DataOut;
reg [31:0] mem[1023:0];
always @(posedge clk)
if (regWE)
mem[Addr] <= DataIn;
initial $readmemb(“file.dat”, mem);
assign DataOut = registers[Addr];
endmodule
$readmemb and $readmemh allow you to load a memory from a file
  b for Binary
  h for Hexadecimal
Done in an initial block
Examples are in the lab3 starter package on the wiki

## Slide 25: = vs <=
= is a blocking assignment
  Evaluate right hand side, assign to left immediately
<= is a non-blocking assignment
  Evaluate right hand side
  Schedule assignment for the end of the time step

## Slide 26: = vs <=: Swap Fest
What are the values of the registers after each clock period?
Which block swaps?
Which block stomps?
always @(posedge clk)
begin
a = b;
b = a;
end
always @(posedge clk)
begin
c <= d;
d <= c;
end
Notes: <= swaps

## Slide 27: = vs <= : Timing
reg a, b, c, d, e, f, g, h, i;
initial begin
#10 a = 1; // a assigned at time 10
#2 b = 0; // b assigned at time 12
#4 c = 1; // c assigned at time 16
end
initial begin
#10 d <= 1; // d assigned at time 10
#2 e <= 0; // e assigned at time 12
$4 f <= 1; // f assigned at time 16
End
initial begin
g <= #10 1; // g assigned at time 10
h <= #2 0; // h assigned at time 2
i<= #4 1; // i assigned at time 4
end
Blocking Assignments
  Each line blocks the next line
Non Blocking Assigments
  Wait statement in scheduling
  The waits cause the blocking
Non Blocking Assignments
  Wait statement in assignment

## Slide 28: = vs <= : TL;DR;
I prefer using <=
  Converts from circuits more naturally
You can use =
  Converts from C code more naturally

## Slide 29: With Remaining Time
Practice / Read about Behavioral Verilog
Work on Final Project Proposals
  Send directly to my email address
  The sooner you submit, the sooner you can start
Work on Lab 3 Planning with your group