## Slide 1: b1010 Advanced Math Stuff
ENGR xD52
Eric VanWyk
Fall 2012

## Slide 2: Acknowledgements
Ray Andraka: A survey of CORDIC algorithms for FPGA based computers
Lumilogic
Jack E. Volder, The CORDIC Trigonometric Computing Technique

## Slide 3: Today
Review Recursive Function Calls
Homework 3
CORDIC: Sines, Cosines, Logarithms, Oh My

## Slide 4: Factorial Function
int Fact(int n){
if(n>1)
return n* Fact(n-1)
else
return 1

## Slide 5: Factorial Function
int Fact(int n){
if(n>1) goto end:
return n* Fact(n-1)
end:
return 1

## Slide 6: Factorial Function
$v0 Fact(int n){
if(n>1) goto end:
$v0 =n* Fact(n-1)
jr $ra
end:
$v0 = 1
jr $ra

## Slide 7: Factorial Function
$v0 Fact ($a0)
ble $a0, 1, end:
$v0 =n* Fact(n-1)
jr $ra
end:
$v0 = 1
jr $ra
We have most of what we need:
  Goto flow control for if
  jr $ra for return
  Registers assigned
Now we need to call Fact
  What do we save?
  What order?
Lets focus on the call site

## Slide 8: Factorial Function Call Site
To Call Fact:
  Push registers I need to save
    $ra
    $a0
  Setup Arguments
    N-1: $a0 = $a0-1
  Jump and Link Fact:
  Restore registers

## Slide 9: Factorial Function Call Site
sub $sp, $sp, 8
sw $ra, 4($sp)
sw $a0, 0($sp)
sub $a0, $a0, 1
jal fact
lw $ra, 4($sp)
lw $a0, 0($sp)
add $sp, $sp, 8
To Call Fact:
  Push $ra, $a0
  Setup $a0
  Jump and Link Fact:
  Restore $ra, $a0

## Slide 10: Factorial Function Call Site
sub $sp, $sp, 8
sw $ra, 4($sp)
sw $a0, 0($sp)
sub $a0, $a0, 1
jal fact
lw $ra, 4($sp)
lw $a0, 0($sp)
add $sp, $sp, 8
To Call Fact:
  Push $ra, $a0
  Setup $a0
  Jump and Link Fact:
  Restore $ra, $a0

## Slide 11: Factorial Function Call Site
sub $sp, $sp, 8
sw $ra, 4($sp)
sw $a0, 0($sp)
sub $a0, $a0, 1
jal fact
lw $ra, 4($sp)
lw $a0, 0($sp)
add $sp, $sp, 8
To Call Fact:
  Push $ra, $a0
  Setup $a0
  Jump and Link Fact:
  Restore $ra, $a0

## Slide 12: Factorial Function Call Site
sub $sp, $sp, 8
sw $ra, 4($sp)
sw $a0, 0($sp)
sub $a0, $a0, 1
jal fact
lw $ra, 4($sp)
lw $a0, 0($sp)
add $sp, $sp, 8
To Call Fact:
  Push $ra, $a0
  Setup $a0
  Jump and Link Fact:
  Restore $ra, $a0

## Slide 13: Factorial Function
fact:
;if(N<=1) return 1
ble $a0, 1, end:
;Push $ra, $a0
sub $sp, $sp, 8
sw $ra, 4($sp)
sw $a0, 0($sp)
;Argument N-1
sub $a0, $a0, 1
jal fact
;Pop $ra, $a0
lw $ra, 4($sp)
lw $a0, 0($sp)
add $sp, $sp, 8
;Return N*Fact(N-1)
mul $v0, $v0, $a0
jr $ra
end:
;Return 1
$v0 = 1
jr $ra

## Slide 14: Calling Function
li $a0, 4
jal factorial
move $s0, $v0
li $a0, 2
jal factorial
move $s1, $v0
li $a0, 7
jal factorial
move $s2, $v0
li $v0, 10
syscall
Calls Factorial several times
Stores results in $sN
li is a pseudoinstruction
  What does it assemble to??
The final two lines call a special simulator function to end execution
  10 means exit
  Look up other syscalls in help

## Slide 15: Key Gotchas
jal calls a subroutine
jr $ra returns from it
Sandwich jal with push and pop pair
  Caller responsible for stack (CDECL)
There are other options, but be consistent!

## Slide 16: Practice
You have 40 minutes. Do any of the following:
Get recursive factorial working and step trace it
Pretend mul&mult don’t exist
  Write a leaf function that does their job with add&shift in a loop.
Write IQ Multiply: IQmult(a, b, Q)
  Multiply two IQN numbers
    IQ24 means I8Q24
  Hint: MULT $t0, $t1 stores the results in $HI$LO
    Retrieve using mfhi and mflo

## Slide 17: Calculating Interesting Functions
So far we have:
  Add, Subtract, And, Or, Shift, Multiply, Divide(ish)
I’ve promised that this can do EVERYTHING
  Square Root, Transcendentals, Trig, Hyperbolics…
How?

## Slide 18: Calculating Interesting Functions
GIANT LUTs
  Because we have silicon area to burn
  Area doubles per bit of accuracy
Power Series and LUTs:
  Approximation by polynomial
  More efficient in space, but still improves slowly
Lets find better ways
  That gain accuracy faster

## Slide 19: CORDIC
Multiplies are expensive in hardware
  So many adders!
Jack Volder invented CORDIC in 1959
  Trig functions using only shifts, adds, LUTs
  We’ll be looking at this half
John Stephen Welther generalized it at HP
  Hyperbolics, exponentials, logs, etc
  This half is awesome too

## Slide 20: CORDIC?
COordinate Rotation DIgital Computer
  A simple way to rotate a vector quickly
Creates rotation matrices based on 2^i
  Makes the math redonkulously quick

## Slide 21: Super Glossy Transformation Step
Start with the basic rotation matrix:
Use trig identities to transform to
Trust Me (or derive on your own)

## Slide 22: The Clever Bit
Pick values of to make the math easy
Now the rotation simplifies to
Store two separate look up tables
  … maybe

## Slide 23: The Result
Rotating a vector is now:
  1 look up, 2 shifts, 3 adds
Optionally Compensate for magnitude at end
  1 lookup, 1 multiply

## Slide 24: Example: Finding the Phase
Given a vector, find
Plan:
Start with
Rotate vector into Quadrant I or IV
Rotate vector until it is flat (zero angle)
  At each iteration, choose direction by sign of Y

## Slide 25: Example: Finding the Phase
Find Phase of -1+3j
Rotate into a start Quadrant
  This is not yet CORDIC

## Slide 26: Example: Finding the Phase I=0
Iteration 0
Y is positive
  Rotate “Down”

## Slide 27: Example: Finding the Phase I=1
Iteration 1
Y is negative
  Rotate “Up”

## Slide 28: Example: Finding the Phase I=2
Iteration 2
Y is zero
  We are done!
Actual answer?

## Slide 29: Example: Finding the Magnitude
Apply the compensations now
5

## Slide 30: Am I lucky or what?!
The example terminated nicely
  Do all start vectors terminate?
  Do all start vectors converge?
Explore the sequence
  How is it shaped?

## Slide 31: The Point?
Area increases linearly per bit of accuracy
Cheap Hardware
Very reusable

## Slide 32: With Remaining Time
Play with CORDIC
  What other functions can it calculate?
Continue with practice from before
Start HW3