## Slide 1: b0100 Floating Point
ENGR xD52
Eric VanWyk
Fall 2012

## Slide 2: Acknowledgements
Mark L. Chang lecture notes for Computer Architecture (Olin ENGR3410)
Patterson & Hennessy: Book & Lecture Notes
Patterson’s 1997 course notes (U.C. Berkeley CS 152, 1997)
Tom Fountain 2000 course notes (Stanford EE182)
Michael Wahl 2000 lecture notes (U. of Siegen CS 3339)
Ben Dugan 2001 lecture notes (UW-CSE 378)
Professor Scott Hauck lecture notes (UW EE 471)
Mark L. Chang lecture notes for Digital Logic (NWU B01)

## Slide 3: Today
Better IQ representation example
Review Multiplication in Fixed Point
Signed/Unsigned and Multiplication
Invent Floating Point Numbers

## Slide 4: Better IQ example

## Slide 5: IQ Multiplication
We ended last class with 3.0 *-0.5 in binary.
3 -> 00110000 I4Q4
-0.5 -> 11111000 I4Q4
-1.5 -> 11101000 I4Q4…?

## Slide 6: Its just like Algebra, right?
  11111000 -0.5 in I4Q4
  * 00110000 3.0 in I4Q4
  00000000
  00000000
  00000000
  00000000
  11111000
  11111000
  00000000
  00000000
  010111010000000 ??? In I?Q?

## Slide 7: Its just like Algebra, right?
  1111.1000 -0.5 in I4Q4
  * 0011.0000 3.0 in I4Q4
  .00000000
  0.0000000
  00.000000
  000.00000
  1111.1000
  11111.000
  000000.00
  0000000.0
  0101110.10000000 46.5 In I8Q8

## Slide 8: Its just like Algebra, right?
  1111.1000 -0.5 in I4Q4
  * 0011.0000 3.0 in I4Q4
  0000000.00000000
  0000000.00000000
  0000000.00000000
  0000000.00000000
  1111111.10000000  I8Q8!!
  1111111.00000000
  0000000.00000000
  0000000.00000000
  11111110.10000000 -1.5 In I8Q8

## Slide 9: Negative Second Operand?
  01.11 I2Q2 d1.75
  * 11.10 I2Q2 –d0.50
  .0000
  0.111
  01.11
  011.1
  0111.
  0111 .
  0111 .
  0111 .
  0111 .
  01101111.0010 I4Q4 -d0.875

## Slide 10: Negative Second Operand?
  01.11 I2Q2 d1.75
  * 11.10 I2Q2 –d0.50
  .0000
  0.111
  01.11
  011.1
  0111.  From sign extension!
  0111 .
  0111 .
  0111 .
  0111 .  No effect on output
  01101111.0010 I4Q4 -d0.875
Notes: Sign extend your second operand vertically until it doesn’t affect the output.
The first four bits are unaffected by sign extension.
The next four need to be valid, which prompts the sign extension vertically.
The last four are unnecessary, and are there just to show the ‘debris’ from the calculation

## Slide 11: Observations
The product is wider than the inputs
  InQx*ImQy=I(n+m)Q(x+y)
Sign extend the inner terms and the multiplicand

## Slide 12: Side Note…
The wikipedia article on binary multipliers is awful.
Prove and rewrite the “More advanced approach: signed integers” section for Awesome.

## Slide 13: Implications
3 categories of integer / IQ multiply instructions:
  MUL N*N->N, sign agnostic (only for Q=0)
  SMUL N*N->2N, signed
  UMUL N*N->2N, unsigned
Multiplication uses ever increasing amounts of memory….?
Notes: The N*N->N sign agnosticism is a neat ‘trick’. I believe it is valid for the first bits up to the lesser of the two input lengths. E.g. I13*I33 are sign agnostic for 13 bits.

## Slide 14: Finite Memory
We can’t expand every time.
Usually, output format is input format.
LSBs dropped are lost precision.
MSBs dropped are occasional catastrophes.
  Bonus Modulo!

## Slide 15: Precision vs Max Magnitude
Humans handle this with scientific notation.
1.234*10^2
Significand * R^Exponent
Significand in I?Q?, Exponent in I?

## Slide 16: Renormalization
We use 0<= Significand < R
  12.34*10^5 looks funny – it is in U2Q2(R10)
  Scientific Notation is U1Q?R10.
What is Engineering Notation?
  123.456*10^7
TLDR: Pick a significand format, stick with it
Notes: U1Q?R1000

## Slide 17: Renormalization
We use 0<= Significand < R
  12.34*10^5 looks funny – it is in U2Q2(R10)
  Scientific Notation is U1Q?R10.
What is Engineering Notation?
  123.456*10^7
TLDR: Pick a significand format, stick with it
Notes: Engineering notation note: IBM mainframes use R16

## Slide 18: Exponent Format
Could use 2’s compliment.
Use ‘biased’ notation instead.
  Signed value ‘biased’ to be unsigned.
  Most negative number becomes 0.
Makes sorting floats easy!

## Slide 19: Multiplication in Floating Point
Easy!
Multiply Significands, Add Exponents
5*10^2 * 4*10^4 = (5*4)*10^(2+4)
= 20*10^6 -> 2.0*10^7

## Slide 20: Addition in Floating Point
Almost Easy!
Operands must have same exponent
  Normalize to most positive exponent
9.8*10^13 + 4*10^12 -> (9.8+0.4)*10^13
  = 10.2*10^13 -> 1.02*10^14

## Slide 21: IEEE-754 Single Precision Float
Floating Point (Float) = (-1)s * (1.significand) * 2(exponent-127)
Alternative Name: binary32
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
significand
s
exponent
1 bit 8 bits 23 bits

## Slide 22: IEEE-754 Single Precision Float
Floating Point (Float) = (-1)s * (1.significand) * 2(exponent-127)
Record Sign bit
Convert Significand to U1Q23
  Track changes to Exponent!
Drop the MSB of Significand, record the rest
  Significand = leading one + Fraction
Bias Exponent by +127, record
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
significand
s
exponent
Notes: Do one on the board:
2.25 -> 10.01 *2^0 -> 1.001 * 2^1
Sign = 0. Expont = 1+127 = 128 = b10000000. Significand = .001
x40100000

## Slide 23: IEEE-754 Single Precision Board Work
Floating Point (Float) = (-1)s * (1.significand) * 2(exponent-127)
Convert to fp hex:
  0.75 -10 .3
Convert from fp: 0x40410100 0xC0FFEE00
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
significand
s
exponent
Notes: 3F400000 C1200000 3E99999A 3F333333
3.015686 -7.9978027
http://www.h-schmidt.net/FloatConverter/IEEE754.html

## Slide 24: Special Cases
Exponent b00000000
  Fraction = 0: Zero
  Fraction!=0: Subnormal
Exponent b11111111
  Fraction = 0: Infinity
  Fraction!= 0: Not a Number

## Slide 25: When things go wrong
Overflow – it too big
Underflow – it too small
Non-Associative – Can’t reorder operations
  Still commutative
  Order determines end precision!
Humans like R10, but it is not representable

## Slide 26: Create your own Pain
Create your own math problems that highlight these four basic problems with floating point math.
You can use decimal for 3 of them
  Pick a format. 2 exponent digits, 7 significand?

## Slide 27: Storage vs Calculation Format
Story Time!

## Slide 28: If you remember nothing else…
Precision: ~7 decimal digits
Relative Error is constant, absolute error varies
Exponent Range: 10^38 10^-38
Represent all integers up to 2^24
Zero is 0x00000000
Infinity is h7F800000, -Infinity is hFF800000
NaN: h7F800001 to h7FFFFFFF
hFF800001 to hFFFFFFFF
h7FC00000 is most common I’ve seen.
Sortable with integer operations
Notes: Relative / absolute error – nano tech vs astronomy

## Slide 29: IEEE-754 Double Precision Float
AKA Binary64
11 exponent bits, 52 explicit significand bits
~16 decimal digits, 10^308 10^-308
All Integers to 2^53
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
significand
s
exponent
31
30
29
28
27
26
25
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
significand (continued)

## Slide 30: Homework
Skim Chapter 3 of Hennessey
Read in depth
  3.4 Division
  3.6 Parallelism and Associativity
  3.7 Real Stuff: Floating point in the x86
  3.8 Fallacies and Pitfalls