## Slide 1: b0111 Performance Anxiety
ENGR xD52
Eric VanWyk
Fall 2012

## Slide 2: Today
What is “Performance”
Measuring Performance
Amdahl’s Law

## Slide 3: Today
J/K Pop Quiz LOL
What is “Performance”
Measuring Performance
Amdahl’s Law

## Slide 4: Pop Quiz!
Work alone
10 minutes
5 Questions
Open Notes

## Slide 5: Pop Quiz
How is the course pacing?
What single topic are you most confused by?
What single topic are you most confident on?
What single request do you want to make?
What is your goal for this course?

## Slide 6: Computer “Performance”
MIPS (Million Instructions Per Second) vs. MHz (Million Cycles Per Second)
Throughput (jobs/seconds) vs. Latency (time to complete a job)
Measuring, Metrics, Evaluation – what is “best”?
The PowerBook G4 outguns Pentium
III-based notebooks by up to 30 percent.*
* Based on Adobe Photoshop tests
comparing a 500MHz PowerBook G4 to
850MHz Pentium III-based portable computers
3.09 GHz
Pentium 4
Hyper
Pipelined
Technology

## Slide 7: Performance Example: Planes
Airplane | Passenger Capacity | Cruising Range (miles) | Cruising Speed (mph) | Passenger Throughput (passengermile/hour)
Boeing 777 | 375 | 4630 | 610 | 228,750
Boeing 747 | 470 | 4150 | 610 | 286,700
Concorde | 132 | 4000 | 1350 | 178,200
Douglas DC8 | 146 | 8720 | 544 | 79,424
Which is the “best” plane?
  Which gets one passenger to the destination first?
  Which moves the most passengers?
  Which goes the furthest?
Which is the “speediest” plane (between Seattle and NY)?
  Latency: how fast is one person moved?
  Throughput: number of people per time moved?

## Slide 8: Computer Performance
Primary goal: execution time (time from program start to program completion)
To compare machines, we say “X is n times faster than Y”
Example: Machine Orange and Grape run a program Orange takes 5 seconds, Grape takes 10 seconds
Orange is _____ times faster than Grape

## Slide 9: Execution Time
Elapsed Time
  counts everything (disk and memory accesses, I/O , etc.)
  a useful number, but often not good for comparison purposes
CPU time
  doesn't count I/O or time spent running other programs
  can be broken up into system time, and user time
Example: Unix “time” command fpga.olin.edu> time javac CircuitViewer.java 3.370u 0.570s 0:12.44 31.6%
Our focus: user CPU time
  time spent executing the lines of code that are "in" our program

## Slide 10: CPU Time
Application example: A program takes 10 seconds on computer Orange, with a 400MHz clock. Our design team is developing a machine Grape with a much higher clock rate, but it will require 1.2 times as many clock cycles. If we want to be able to run the program in 6 second, how fast must the clock rate be?
CPU execution time
for a program
CPU clock cycles
for a program
Clock period
=
*
CPU execution time
for a program
CPU clock cycles
for a program
1
Clock rate
=
*

## Slide 11: CPI
How do the # of instructions in a program relate to the execution time?
CPU clock cycles
for a program
Instructions
for a program
Average Clock
Cycles per Instruction
(CPI)
=
*
CPU execution time
for a program
Instructions
for a program
=
*
1
Clock rate
*
CPI

## Slide 12: CPI Example
Suppose we have two implementations of the same instruction set (ISA).
For some program Machine A has a clock cycle time of 10 ns. and a CPI of 2.0 Machine B has a clock cycle time of 20 ns. and a CPI of 1.2
What machine is faster for this program, and by how much?

## Slide 13: Computing CPI
Different types of instructions can take very different amounts of cycles
Memory accesses, integer math, floating point, control flow
Instruction Type | Type Cycles | Type Frequency | Cycles * Freq
ALU | 1 | 50% | 
Load | 5 | 20% | 
Store | 3 | 10% | 
Branch | 2 | 20% | 
 |  | CPI: | 
Notes: .5 + 1 + .3 + .4 = 2.2

## Slide 14: CPI & Processor Tradeoffs
How much faster would the machine be if:
A data cache reduced the average load time to 2 cycles?
Branch prediction shaved a cycle off the branch time?
Two ALU instructions could be executed at once?
Instruction Type | Type Cycles | Type Frequency
ALU | 1 | 50%
Load | 5 | 20%
Store | 3 | 10%
Branch | 2 | 20%
Notes: 1.375
1.1
1.22

## Slide 15: Warning 1: Amdahl’s Law
The impact of a performance improvement is limited by what is NOT improved:
Example: Assume a program runs in 100 seconds on a machine, with multiply responsible for 80 seconds of this time. How much do we have to speed up multiply to make the program run 4 times faster?
5 times faster?
Execution time
after improvement
Execution time
of unaffected
=
*
1
Amount of improvement
+
Execution time affected
Notes: 100/4 = 25
25 – 20 = 5
80/5 = 16 times faster
INFINITY

## Slide 16: Warning 2: MIPs, MHz  Performance
Higher MHz (clock rate) doesn’t always mean better CPU
Orange computer: 1000 MHz, CPI: 2.5, 1 billion instruction program
Grape computer: 500MHz, CPI: 1.1, 1 billion instruction program
Higher MIPs (million instructions per second) doesn’t always mean better CPU
1 MHz machine, with two different compilers/instruction sets
Compiler A on program X: 10M ALU, 1M Load
Compiler B on program X: 5M ALU, 1M Load
  Execution Time: A ____ B ____
  MIPS: A ____ B ____
Instruction Type | Type Cycles
ALU | 1
Load | 5
Store | 3
Branch | 2

## Slide 17: Processor Performance Summary
Machine performance:
Better performance:
_____ number of instructions to implement computations
_____ CPI
_____ Clock rate
Improving performance must balance each constraint
Example: RISC vs. CISC
CPU execution time
for a program
Instructions
for a program
=
*
1
Clock rate
*
CPI
Notes: Lower is better
Lower is better
Higher is better

## Slide 18: Board Work Fun Times
Pick one element and make 2 designs
  Adder -- Subtractor
  Shifter -- Multiplier (N->N? N->2N?)
Calculate/Estimate:
  Clocks Per Instruction
  Propagation delay
  Number of gate inputs ($)

## Slide 19: Board Work Results
We now have several construction options
Which elements dominate clock speed?
Which elements should we spend space on?
Which elements can we make more compact?