## Slide 1: b 0000 Pipelining
ENGR xD52
Eric VanWyk
Fall 2012
1

## Slide 2: Acknowledgements
Mark L. Chang lecture notes for Computer Architecture (Olin ENGR3410)

## Slide 3: Today
The Best Computer Architecture Slide Ever
Introduction to Pipelining
Reasons to Pipeline
DIY Pipelined CPUs
Hazards

## Slide 4: Single Cycle, Multiple Cycle, vs. Pipeline
Clk
Cycle 1
Multiple Cycle Implementation:
Ifetch
Reg
Exec
Mem
Wr
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Load
Ifetch
Reg
Exec
Mem
Wr
Ifetch
Reg
Exec
Mem
Load
Store
Pipeline Implementation:
Ifetch
Reg
Exec
Mem
Wr
Store
Clk
Single Cycle Implementation:
Load
Store
Waste
Ifetch
R-type
Ifetch
Reg
Exec
Mem
Wr
R-type
Cycle 1
Cycle 2

## Slide 5: Recap
Single Cycle CPUs
  Speed limited by the slowest instruction
Multi Cycle divides instr into multiple chunks
  as slow as slowest chunk
  Uses variable CPI for speed up
Which is faster on average?
When is the other option faster? Why?

## Slide 6: Pipelining
Example: Doing the laundry
Ann, Brian, Cathy, & Dave
each have one load of clothes to wash, dry, and fold
Washer takes 30 minutes
Dryer takes 40 minutes
“Folder” takes 20 minutes
A
B
C
D

## Slide 7: Sequential Laundry
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?

## Slide 8: Pipelined Laundry: Start work ASAP
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 9
A
B
C
D
6 PM
7
8
9
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduces speedup
Pipelining Lessons

## Slide 10: Pipelined Execution
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
Program Flow
Time
CPI in pipelined processor is “issue rate”
Ignore fill/drain, ignore latency
Pipelining maximizes throughput

## Slide 11: Single Cycle, Multiple Cycle, vs. Pipeline
Clk
Cycle 1
Multiple Cycle Implementation:
Ifetch
Reg
Exec
Mem
Wr
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Load
Ifetch
Reg
Exec
Mem
Wr
Ifetch
Reg
Exec
Mem
Load
Store
Pipeline Implementation:
Ifetch
Reg
Exec
Mem
Wr
Store
Clk
Single Cycle Implementation:
Load
Store
Waste
Ifetch
R-type
Ifetch
Reg
Exec
Mem
Wr
R-type
Cycle 1
Cycle 2

## Slide 12: Why Pipeline?
Suppose we execute 100 instructions
Single Cycle Machine
  45 ns/cycle x 1 CPI x 100 inst = ____ ns
Multicycle Machine
  10 ns/cycle x 4.0 CPI x 100 inst = ____ ns
Ideal pipelined machine
  10 ns/cycle x (1 CPI x 100 inst + 4 cycle drain) = ____ ns
Notes: 4500 ns
4000 ns
1040 ns

## Slide 13: Rules of Pipelining
Divide CPU / Instruction in to stages
Each functional unit belongs to one stage
  Can’t reuse the e.g. ALU like a multi-cycle design
  Reg File ports are different functional units
  For now, split memory into instruction & data
Stage order is the same for all instructions
  How to “skip” a stage?
  This is true for “purely” pipelined processors

## Slide 14: Pipelined Datapath
Registers
Registers
Registers
Registers
Divide datapath into multiple pipeline stages
PC
Data
Memory
Instr.
Memory
Register
File
Register
File
IF
Instruction
Fetch
RF
Register
Fetch
EX
Execute
MEM
Data
Memory
WB
Writeback

## Slide 15: Pipelined Control
IF/ID Register
ID/Ex Register
Ex/Mem Register
Mem/Wr Register
Reg/Dec
Exec
Mem
ALUSrcA
ALUOp
RegDst
ALUSrcB
IorD
MemWE
Mem2Reg
RegWE
Main
Control
ALUSrcA
ALUOp
RegDst
ALUSrcB
Mem2Reg
RegWE
Mem2Reg
RegWE
Mem2Reg
RegWE
IorD
MemWE
IorD
MemWE
Wr
The Main Control generates the control signals during Reg/Dec
  Control signals for Exec (ALUOp, ALUSrcA, …) are used 1 cycle later
  Control signals for Mem (MemWE, IorD, …) are used 2 cycles later
  Control signals for Wr (Mem2Reg, RegWE, …) are used 3 cycles later

## Slide 16: Pipelining the Load Instruction
The five independent functional units in the pipeline datapath are:
  Instruction Memory for the Ifetch stage
  Register File’s Read ports (bus A and busB) for the Reg/Dec stage
  ALU for the Exec stage
  Data Memory for the Mem stage
  Register File’s Write port (bus W) for the Wr stage
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Ifetch
Reg/Dec
Exec
Mem
Wr
1st lw
Ifetch
Reg/Dec
Exec
Mem
Wr
2nd lw
Ifetch
Reg/Dec
Exec
Mem
Wr
3rd lw

## Slide 17: The Four Stages of R-type
Ifetch: Fetch the instruction from the Instruction Memory
Reg/Dec: Register Fetch and Instruction Decode
Exec: ALU operates on the two register operands
Wr: Write the ALU output back to the register file
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Ifetch
Reg/Dec
Exec
Wr
R-type

## Slide 18: Structural Hazard
Interaction between R-type and loads causes structural hazard on writeback
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type

## Slide 19: Structural Hazard
Interaction between R-type and loads causes structural hazard on writeback
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type

## Slide 20: Structural Hazard: Solved
Add a do-nothing (NO OP or NOP) MEM stage
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Exec
Exec
Exec
Exec

## Slide 21: DIY Pipelining
Design your own Pipelined MIPS CPU
  ADD, LW, SW,
  J, JAL if you have time. BEQ if you are rocking it
Start with a 5 stage pipeline:
  Instruction Fetch
  Instruction Decode / Register Fetch
  Execute
  Data Memory
  Register Write Back
You can merge / split cycles if you’d like

## Slide 22: DIY Pipelining
Deliverables:
  Schematic of Data path (stub out control signals)
  Control signals chart for instructions
  Pipeline chart for instructions
Pretend to execute a simple program
  Use a homework or lecture program?
  Make a pipeline chart for this program

## Slide 23: DIY Pipelining
Record hazards you encounter in your design
  Trying to double use a functional unit?
  Trying to use information before it is ready?
  Can you rewrite your program to avoid them?
    Specifically when is this possible?
These will be the basis of Monday’s class
  Come back with one specific hazard