## Slide 1: b1111 Timing and Control
ENGR xD52
Eric VanWyk
Fall 2012

## Slide 2: Acknowledgements

## Slide 3: Today
Controlling a Multi Cycle CPU
Balancing Cycles
More Multi Cycle Board Work
  With Hints of MicroOps!

## Slide 4: Decoding Instructions
Decoder for Single Cycle CPU: Look Up Table
  Depth = OpCodes
  Width = # Control Signal Bits
Multicycle adds states to the decoding
Use a Finite State Machine to track these

## Slide 5: Finite State Machines
A group of States and Transitions
Move from one state to another along a transition line when the transition’s conditions are met
Heater Off
Heater On
Temp <68F
Temp >72F

## Slide 6: Flying Spaghetti Monsters
In Computer Architecture, FSMs:
  Usually transition on a clock edge
  Are Complete
    All states define transitions for all inputs
  Are deterministic (Unless Quantum)
Heater Off
Heater On
Temp <68F
Temp >72F

## Slide 7: FSM Implementation
Register to hold current state
Wires to provide inputs (arguments)
Look Up Table(s) to map transitions
Current State | Inputs | Resulting State
Heater Off | Too Cold | Heater On
Heater Off | --- | Heater Off
Heater On | Too Hot | Heater Off
Heater On | --- | Heater On
Control Logic
(LUTs)
Inputs
Register
Controls

## Slide 8: All Hail Our Partial FSM
Each Phase becomes an FSM State
Most states have only one transition that is always taken
  no conditions
Note the Re-Use!
IFetch
Decode
Store 1
Load 1
Load 2
Load 3
Store 2
Op = = 43
Op = = 35

## Slide 9: Process
Enumerate states
Assign Values
Calculate Width
Make a LUT
State | Inputs | Next State
IFetch | X | Decode
Decode | Op==43 | Store 1
Decode | Op==35 | Load 1
Store 1 | X | Store 2
Store 2 | X | IFetch
Load 1 | X | Load 2
Load 2 | X | Load 3
Load 3 | X | IFetch

## Slide 10: Process
Enumerate states
Assign Values
Calculate Widths
Make a LUT
State | Inputs | Next State
0 | X | 1
1 | Op==43 | 2
1 | Op==35 | 4
2 | X | 3
3 | X | 0
4 | X | 5
5 | X | 6
6 | X | 0

## Slide 11: Process
Enumerate states
Assign Values
Calculate Widths
  Width = 8
Make a LUT
State[0:3] | Inputs[0:5] | Next State
0 | X | 1
1 | Op==43 | 2
1 | Op==35 | 4
2 | X | 3
3 | X | 0
4 | X | 5
5 | X | 6
6 | X | 0

## Slide 12: 2 LUTs 1 State Machine
Control signals only depend on the state
  Not the other inputs
  “Moore Machine” vs “Mealy Machine”
Split Control Logic in to two separate LUTs
  Control Signals: Shallow & Wide
  State Updates: Deep and Narrow
  Better use of space
  What parts can be shared?

## Slide 13: Balance
An unbalanced design has some operations doing more “work” (time) than the others
  Wastes time in fast cycles
Moving work between operations is Balancing
  Reduce the global clock period by leveling
Balance adjacent ops by register positioning
  Some ops are hard to “slice”

## Slide 14: Example
Instruction has 5 components:
  1, 2, 3, 4, and 5 nanoseconds long
  In that order
Divide optimally in to 3 operations:
  Minimum Clock Period?
  How much time is wasted per instruction?

## Slide 15: Example
Instruction has 5 components:
  1, 2, 3, 4, and 5 nanoseconds long
  In that order
Divide optimally in to 3 cycles:
  Minimum Clock Period? 6ns
  How much time is wasted per instruction? 3ns
  {1,2,3}{4}{5}

## Slide 16: Balancing
Not all resources are fungible
  Some micro-operations are hard to subdivide
  Order of operations matters sometimes
The slowest unit sets the pace for everything
Compare “Optimal” time to Reality
  Measure of Balance

## Slide 17: Example Timings
Instr/Cycle | RTL | Symbolic | Numeric
LW:0 | IR = Mem[PC] | tX1 + tMEM | 10
LW:0 | PC=PC+4 | tX1+tALU+tX2 tX2+tALU+tX2 | 5 5
LW:1 | AB = RegFile[_] | tRF | 3
LW:2 | Res = A + SEI | tALU | 5
LW:3 | DR = Mem[Res] | tX1 + tMEM | 10
LW:4 | RegFile[rs] = DR | tRF+tX1 | 3
Component | Symbol | Delay
ALU | tALU | 5ns
Register File | tRF | 3ns
Instruction/Data Memory | tMEM | 10ns
Muxes (Optional) | tXn | 0ish
Registers | 0 | 0

## Slide 18: Multi Cycle w/ Controls
SignExtnd
PC
<<2
MDR
ALU RES
B
A
WrEn
Addr Dout
Memory
Din
IR
Rs
Rt
Rd
Imm16
Aw Ab Aa
Da
Registers
Dw WrEn Db
4
MemIn
Mem_WE
IR_WE
PC_WE
RegIn
Dst
Reg_WE
ALUSrcA
ALUSrcB
ALUOp
PCSrc
Concat

## Slide 19: With Remaining Time
Create the FSM & LUT for your Multicycle
Look for inefficiencies
  How could you reduce the area cost of this?
Time your Multicycle design from Monday
  Do symbolically first, then substitute real numbers
  Remember parallel paths!

## Slide 20: Bonus Work
Calculate Execution time of a program with
  10,000 Instructions
  50% Add-like instructions
  20% Load, 10% Store, 10% Branch, 10% Jump
  Find & Measure one way to improve this
    Balancing? Combining Cycles?
Compare to Single Cycle
Notes: 10ns per cycle
4*.5 + 5*.2 + 3*.1 + 2*.1 = 3.5CPI = 350 microseconds

## Slide 21: Ultra Bonus Work
Implement Shift-Left-as-a-loop in the decoder
  Start Adding!
  Draw the FSM, don’t bother with the LUT
  How many cycles does it take? Cycle Time?
Shift-With-A-Barrel-Shifter in the ALU
  Assume ALU is now 3x slower than before
    Just For Giggles
  How many cycles does the total instruction take?
  New Cycle Time?
What percent of our ALU ops need to be SLL to justify using a hardware barrel shifter?

## Slide 22
SignExtnd
PC
Addr[31:2]
Addr[1:0]
Instruction
Memory
Concatenate
Adder
Instr[31:0]
“00”
PC[31:28]
Target Instr[25:0]
imm16
“1”
Branch
Cin
“0”
0 1
0 1
SignExtnd
WrEn Addr
Din Dout
Data
Memory
Rs
Rt
imm16
ALUSrc
RegDst
Rd
Rt
ALUcntrl
Aw Aa Ab Da
Dw Db
Register
WrEn File
RegWr
MemWr
MemToReg
Zero
Rs
Rt
Rd
Imm16
[25:21]
[20:16]
[15:11]
[15:0]
Notes: Single Cycle CPU

## Slide 23: Conclusions?
What was the original balancing penalty?
  After Improvement?
How did it compare to Single Cycle?
  Where were the gains? Losses?